## Slide 1
VENDING MACHINE
Sahitya Kushwaha (623195)
Prasastha Datla (623157)
Ganti Dheeraj (623192)
EC 202 Presentation

## Slide 2
    Debounce Module
    Slow Clock Generator
    Flip-Flop Module
    Binary to BCD Converter
    7-Segment Driver and Decoder
    Vending Machine
Main Components

## Slide 3
Module: Top_Module
Inputs: clk, reset, btn1, btn2, btn3, sw[7:0]
Outputs: led, seg, an, dp
Description: Integrates all submodules and connects signals for the vending machine functionality
Top Module

## Slide 4
Purpose: Debounce button signals to avoid erroneous inputs.
Inputs/Outputs:
Inputs: clk_in, pb
Outputs: led
Working:
Uses a 4 Hz slow clock and two D flip-flops to debounce the input.
Debounce Module

## Slide 5
Purpose: Generate a 4 Hz clock signal from the input clock.
Inputs/Outputs:
Input: clk_in
Output: clk_out
Description:
Counts up to 12,500,000 to toggle clk_out at 4 Hz.
Slow Clock 4Hz Module

## Slide 6
Purpose: Basic D flip-flop with output and complemented output.
Inputs/Outputs:
Inputs: clk, D
Outputs: Q, Qbar
Flip-Flop Module

## Slide 7
Purpose: Convert a 12-bit binary number to BCD format.
Inputs/Outputs:
Input: binary[11:0]
Outputs: thos, hund, tens, ones
Operation: Divides and finds the remainder to convert binary to decimal.
Binary to BCD Converter Module

## Slide 8
Purpose: Display BCD digits on a 7-segment display.
State Machine: Cycles through four states to display each digit.
Code Overview:
Inputs: clk, clr, BCD digits
Outputs: seg, an, dp
7-Segment Driver Module

## Slide 9
Purpose: Display each digit on a 7-segment display.
State Machine: turns on the LEDs to display corresponding digits on screen
Code Overview:
Inputs: clk, clr, BCD digits
Outputs: seg, an, dp
7-Segment Decoder Module

## Slide 10
Purpose: Handles vending operations and tracks money and stock.
Inputs/Outputs:
Inputs: clk, reset, twenty, fifty, select, buy, load
Outputs: money, products, out_of_stock
Key Operations:
Accepts money, handles purchases, and manages stock.
Vending Machine Module

## Slide 11
Discussed the integration of all modules to form a complete vending machine system
Open for any questions.
Conclusion

## Slide 12
1. Commercialization and Real-world Application
Prototype for Production: Develop a physical prototype to demonstrate the feasibility of deploying the system in real-world vending machines.
2. Robotic Dispensing System
  Dual Dispenser: Allow simultaneous dispensing of different types of products for faster service.
  adding more no. of products
Further Improvements

## Slide 13
THANK YOU